Supporting Information

Theoretical Background of Dynamic Nuclear Polarization

The general theory of Dynamic Nuclear Polarization is well described elsewhere[1,2]. Here only the specific case of the interaction between an electron spin S carried by a radical species and a proton spin I in liquids in a constant magnetic field B0 shall be considered. More details can be found in the litterature[3-10].

The Overhauser effect (E) on spin I that occurs upon EPR irradiation (usually by microwaves) of spin S coupled to it can be calculated as:

(A1)

where IZ and I0 are the observed and equilibrium polarization of the nuclear spin, SZ and S0 the observed and equilibrium polarization of the electron spin,  the electron-nucleus coupling constant and f the leakage factor.

Assuming a pure dipolar interaction under the extreme narrowing limit, the electron-nucleus coupling constant  can be approximated to ½.  The leakage factor f represents the part of the electron-nucleus interaction in the longitudinal relaxation of the nucleus:

(A2)

where T1I and T1I0 are the T1 values of the nucleus observed in the presence and the absence of the radical species. Knowing the spin-lattice relaxivity r1 and the concentration c of the latter, f can be written as:

(A3)

The saturation factor s of spin S induced by EPR irradiation can be introduced in the formulation of the Overhauser effect E as:

(A4)

where S and I are the magnetogyric ratio of the corresponding spins. The saturation factor is described as:

(A5)

where T1S and T2S are the spin-lattice and the spin-spin relaxation time constants of spin S, B1 the irradiating magnetic field oscillating at angular frequency ( and (S the resonance frequency of the electron. The value of s ranges from zero in case of no saturation to unity in case of complete saturation.

In case of an additional hyperfine coupling of the electron with an adjacent nucleus K, a number of possible transitions between spin states can occur hence resonance splitting of the EPR lines. In nitroxides the electron is coupled with a hyperfine constant ASK to the 14N nucleus (K=1). Six spin states can then be defined and 6 possible transitions. At “high fields” (), only 3 transitions between spin states are considered, with 3 resonances in the nitroxide EPR spectrum. As only one EPR line can be saturated, the Overhauser effect is divided by the multiplicity n (n=3).

Taking into account the saturation time TS of a given EPR line the Overhauser effect can be written as:

(A6)

Under the experimental conditions of the present study, the maximal value for E, i.e. the maximal possible enhancement in the MRI signal, is around 110.

1. Overhauser AW (1953) Polarization of nuclei in metals. Phys Rev: 411-412.

2. Abragam A, Combrisson J, Solomon I (1957) Compt Rend Acad Sci Paris: 157.

3. Abragam A (1978) Principles of Dynamic Nuclear Polarization. Rep Prog Phys 41: 395-467.

4. Hausser KH, Stehlik D (1968) Dynamic Nuclear Polarization in Liquids. Adv Magn Reson 3: 79-139.

5. Dwek RA, Richards RE, Taylor D (1969) Nuclear Electron Double Resonance in Liquids. Ann Rev NMR Spectr 2: 293-344.

6. Guiberteau T, Grucker D (1993) Dynamic Nuclear Polarization of Water Protons by Saturation of s and p EPR Transitions of Nitroxides. J Magn Reson A 105: 98-103.

7. Guiberteau T (1994) Polarisation dynamique en champ magnétique faible : Application à la spectroscopie et à l’oxymétrie. Strasbourg, France: Université Louis Pasteur.

8. Grucker D, Guiberteau T, Eclancher B, Chambron J, Chiarelli R, et al. (1995) Dynamic Nuclear Polarization with Nitroxides Dissolved in Biological Fluids. J Magn Reson B 106: 101-109.

9. Guiberteau T, Grucker D (1996) EPR Spectroscopy by Dynamic Nuclear Polarization in Low Magnetic Field. J Magn Reson B 110: 47-54.

10. Ardenkjaer-Larsen JH, Laursen I, Leunbach I, Ehnholm G, Wistrand LG, et al. (1998) EPR and DNP properties of certain novel single electron contrast agents intended for oximetric imaging. J Magn Reson 133: 1-12.