# Appendix B: Derivation of equations F2 and D2

Rigorous derivation of equation (F2; Table 2) follows from the basic assumptions of DEB theory [16, 32]. A somewhat simplified approach is also presented in literature [45]. From Figure 1, the mass balance for the reserve density, , can be written

, (B1)

In DEB theory, reserve density determines the chemical composition of organisms; a property directly related to the homeostasis assumption. Therefore, the homeostasis assumption greatly restrict the reserve density dynamics in the sense that, at constant food level , the chemical composition of organisms does not change. After introducing the structural length , and noting that , the homeostasis assumption requires that

, (B2)

because at  the reserve density does not depend on size, i.e. , where  and  are yet undetermined functions. Let us first determine the function  by noting that the reserve density  depends on food level , while the utilization of reserve is assumed to be only a function of state variables, i.e.  (intuitively, the reserve “filters” high frequency changes occurring in the environment and secures the stability of internal conditions). This is possible only if . Comparing equations (B1) and (B2) now yields

. (B3)

A simplified approach [45] determines the function  by directly assuming the first order regulatory process for the reserve density dynamics, i.e. , where  is the model parameter. More formal approaches [16, 32] consider the metabolic stoichiometry, which states that reserve is transformed into structure (V) and metabolites, M1 to Mz, according to the (stylized) chemical reaction

, (B4)

with cG, a1 to az being the stoichiometric coefficients in C-moles. If reserve is divided into  and , where , then

, (B5)

must be valid, because otherwise the chemical composition of reserve will change – a violation of the homeostasis assumption. This also implies . From equation (B3), for a fully grown adult, we then have , which means that the regulatory process for the reserve density is indeed a first order process, i.e. . Inserting the last expression into equation (B3) results in a relationship equivalent to (F2; Table 2). To include the shape correction, a substitute  is necessary. Subsequent application of the κ-rule produces the rightmost expression in (F2; Table 2).

Equation (D2; Table 3) is a mathematical statement of assumption that a part of mobilized reserve is invested into the growth of structure (Figure 1). Since the chemical composition of reserve and structure differs, to produce a unit of structure V  costs  units of energy from reserve. This can be written

. (B6)

Introducing the structural length, , into the above equation results in

, (B7)

which is equivalent to equation (D2; Table 3).